## Slide 1
Compiler-Driven EPR
Pre-Generation
Physical validation, memory trade-offs, and reproducible evidence
BTP Research Project · September 2026

## Slide 2
BTP · Compiler-Driven ACE
Research question
Can compiler knowledge prepare the exact EPR pair early enough to reduce request service latency?
Compiler trace
future A → B requests
Request-specific
preparation
Physical generation
retry and memory noise
Exact pair at use
or demand fallback
Measure readiness, service latency, fidelity at use, expiry, fallback, and pair identity.

## Slide 3
BTP · Compiler-Driven ACE
From scheduling model to physical evidence
Topology-correct
control routing
Analytical
ODG / CGP / ACGP
Native SeQUeNCe
physical execution
ACE lifecycle
and provenance repair
Contracts and
identity audits
The analytical model chooses policies. Physical backends execute stochastic generation, retries, decoherence, and fallback.

## Slide 4
BTP · Compiler-Driven ACE
Locked experimental workload
4×4
mesh, 16 cores
96
logical qubits
4,954
inter-core transfers
2,831
conflict-free sublayers
30
paired seeds per cell
Trace SHA-256 61d97492195aea40fad48d5bc4e1b48b2dd019eea20fe24aada8c954e3073da1

## Slide 5
BTP · Compiler-Driven ACE
What makes a numerical result auditable
Immutable contract
Paired seeds 0–29
Raw runs.json
Trace hash
Completion audit
Pair-identity audit
A seed-zero run is a smoke test. Final claims require all 30 paired replications and passing audits.

## Slide 6
BTP · Compiler-Driven ACE
ACE fixed-lead sensitivity
Audited static 3+1, 2+2, 1+1 and shared-pool matrices · 30 paired seeds per point
Chart: 
| Δ1 | Δ2 | Δ3 | Δ4 | Δ5 | Δ6
Static 3+1 | 0.5531 | 0.63323 | 0.69735 | 0.73266 | 0.77208 | 0.80797
Static 2+2 | 0.72084 | 0.80568 | 0.84686 | 0.86527 | 0.89003 | 0.91923
Static 1+1 | 0.91087 | 0.90869 | 0.94386 | 0.95972 | 0.97947 | 0.99428
Shared pool | 0.59828 | 0.63519 | 0.72604 | 0.74616 | 0.7845 | 0.8186
Δ1 best latency
Static 3+1
Δ1 best latency
Static 2+2 and shared pool
Δ2 lowest mean
Static 1+1
The 1+1 Δ1/Δ2 difference is 0.002186 ms. Interpret it using paired raw data.

## Slide 7
BTP · Compiler-Driven ACE
Shared-pool fixed-lead trade-offs
Legacy cap-three admission, 30 paired seeds per lead
Chart: 
| Δ1 | Δ2 | Δ3 | Δ4 | Δ5 | Δ6
Pre-ready | 59.17 | 54.72 | 44.15 | 41.91 | 37.25 | 33.56
Fallback | 40.8 | 45.26 | 55.82 | 58.09 | 62.75 | 66.44
Expiry | 55.32 | 57.18 | 58.68 | 59.64 | 61.44 | 62.66
Chart: 
| Δ1 | Δ2 | Δ3 | Δ4 | Δ5 | Δ6
Fidelity at use | 0.8584 | 0.7856 | 0.7732 | 0.7344 | 0.7035 | 0.653

## Slide 8
BTP · Compiler-Driven ACE
Why demand fallback remains necessary
Chart: 
| Fixed | Dynamic
Completed | 2793 | 3602
Terminal misses | 2161 | 1352
Strict compiler-only 4+0
Seed-zero coverage diagnostic
No demand fallback
Compiler knowledge does not eliminate finite capacity, physical failure, or missed deadlines.

## Slide 9
BTP · Compiler-Driven ACE
ACE adaptive baselines and compiler scheduling
Historical shared-pool Δ2 snapshot
Chart: 
| ODG | CGP | ACGP | Fixed Δ2 | Dynamic
Latency (ms) | 1.1042 | 0.54773 | 0.4763 | 0.65847 | 0.61591
Lowest latency
ACGP 0.476 ms
Lowest compiler expiry
Dynamic 14.32%
Historical fixed row
uses Δ2 only

## Slide 10
BTP · Compiler-Driven ACE
ACE and native answer complementary questions
ACE
Native SeQUeNCe
Adaptive reservation/cache lifecycle
Application-service latency endpoint
Barrett–Kok generation, retries, swapping,
teleportation, receiver correction
Compare policy direction and trade-offs within one backend

## Slide 11
BTP · Compiler-Driven ACE
Next research controls
Cap-four wait-on-demand
Atomic endpoint allocation
Pending-demand priority
Native fixed-lead matrices
Static and shared pool
Δ1 through Δ6
Compiler routing
Offline path planning
Adaptive runtime route choice
Every final number will retain an immutable contract, 30 paired seeds, trace hash, raw provenance, and identity audit.

## Slide 12
Current evidence
ACE fixed-lead sensitivity: completed and audited
ACE static 3+1, 2+2, 1+1: completed and audited
Shared-pool atomic cap-four: implemented control, final matrix pending
Native fixed-lead and adaptive matrices: pending audit
Thank you